Introduction to the ToolBus Coordination Architecture
Paul Klint

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
The problem: component interconnection
Systems become heterogeneous because we want to couple existing and new software components
  - different implementation languages
  - different implementation platforms
  - different user-interfaces
Systems become distributed in local area networks
Needed: interoperability of heterogenous systems

---
Component interconnection: reasons
Reusing existing components decreases construction costs of new systems
Decomposing large, monolithic systems into smaller, cooperating components increases
  - modularity
  - flexibility

---
Component interconnection: issues
Data integration: exchange of data between components
Control integration: flow of control between components
User-interface integration: how do the user-interfaces of components cooperate?

---
Data integration
Data representations differ per
  - machine: word size, byte order, floating point representation, ...
  - language implementation: size of integers, emulation of IEEE floating point standard, ...
How can we exchange data between components:
  - integers, reals, record => linear encoding
  - pointers => impossible in general

---
Data integration
Assume a common representation R
For each component Ci (with data domain Di) there exist conversion functions
  - fi : Di -> R and fi-1: R -> Di
  - Convert a value di from Ci to Cj by fj-1(fi(di))
Examples: IDDL, ASN-1, ...
ToolBus uses ATerms as common representation

---
Control integration
Broadcasting: each component can notify other components of state changes
Remote procedure calls: components can call each other as procedures
General message passing: the most general approach
In the ToolBus Tscripts are used to model the interactions between components

---
User-interface integration
There is a general trend towards multi-threaded user-interfaces (concurrency)
There is a general trend to use formal techniques to specify user-interfaces
The ToolBus does not address user-interface integration as separate issue but can be used to achieve it

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
Brief history of the ToolBus
Around 1992 the first implementation of the ASF+SDF Meta-Environment was completed:
  - 200 KLOC Lisp code
  - Monolithic
  - Hard to maintain
... all traits of a legacy system

---
Time line
1992: Unsuccessful decomposition experiments
1994: First ToolBus
1995: Discrete time ToolBus
2001: Meta-Environment restructured
2002/3: preparing for the next generation ...

---
1992
Emacs
Graphical Objects
User-interface
Structure & text
editor
Structure editor
Other parts
Other parts
New
Old

---
1993
Difficult synchronization and communication problems problems start to appear
PSF specification of communication; simulation reveals several deadlocks
Problems with this specification:
  - complex (> 20 pages) and ad hoc
  - difficult to extend
  - cannot be used to directly coordinate the components

---
1993/1994
Idea of a “ToolBus” as general communication structure appeared
First design and implementation
Several experiments
  - Feature interaction in telephone switches (RUU/PTT)
  - Traffic control (Nederland Haarlem/UvA/CWI/RUU)
  - Management of complex bus stations (idem)
  - Definition of user interfaces (UvA)

---
1994/1995
Fall 1994: redesign based on this experience
Spring 1995: design and implementation of Discrete Time ToolBus completed
First experiments to prototype parts of the Meta-Environment started

---
More recently ...
In 2001 a new implementation of the Meta-Environment based on the ToolBus was completed
End 2002 we have started on a new generation ToolBus based on these experiences ...

---
ToolBus requirements
Flexible interconnection architecture for software components
Good control over communication
Relatively simple descriptions
Uniform data exchange format
Multi-lingual: C, Java, Perl, ASF+SDF, ...
Potential for verification
Use existing concurrency theory

---
Coordination, Representation & Computation
Coordination: the way in which program and system parts interact (procedure calls, RMI, ...)
Representation: language and machine neutral data exchanged between components
Computation: program code that carries out a specialized task
A rigorous separation of coordination
from computation is the key to
flexible and reusable systems

---
Architectural Layers
Coordination
Representation
Computation
Cooperating Components
Single Component
Single Component
Representation
Computation

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
Generic Representation
Annotated Terms (ATerms)
Applicative, prefix terms
Maximal subterm sharing ( DAG)
  - cheap equality test, efficient rewriting
  - automatic generational garbage collection
Annotations (text coordinates, dataflow info, ...)
Very concise, binary, sharing preserving encoding
Language & machine independent exchange format

---
ATerms
Term and Annotations
Annotations

---
A term is ...
a Boolean, integer, real or string
  - true, 37, 3.14e-12, “rose”
a value occurrence of a variable
  - X, InitialAmount, Highest-bid
a result occurrence of a variable
  - X?, InitialAmount?

---
A term is ...
a single identifier
  - f, pair, zero
a function application
  - pair(“rose”, address(“Street”, 12345))
a list
  - [a, b, c], [a, 1.25, “last”], [[a, 1], [b, 2]]
a placeholder
  - <int>, add(<int>,<int>)

---
Matching of terms
Term matching is used to
  - determine which actions can communicate
  - to transfer data between sender and receiver
Intuition:
  - terms match if the are structurally identical
  - value occurrence: use variable's value
  - result occurrence: assign matched subterm to variable (only if overall match succeeds!)

---
Example of term matching
Before match
X : 3
Y : 7
Z : 17
Context 1
Context 2
Match
f(X,4,Y?,6) and f(3,Z?,5,6)
After successful match
X : 3
Y : 5
Z : 4
Context 1
Context 2

---
Types
The ToolBus uses its own type system
  - static checks & automatic generation of interface code
bool, int, real, str
list: list with arbitrary elements
list(Type): list with Type elements
  - list(int)
term: arbitrary term

---
Types
Id: all terms with function symbol Id (allows partial type declarations)
  - f accepts f, f(1), f(“abc”,3), ...
Id(T1, ..., Tn)
  - f(int, str) accepts f(3,”abc”) but not f(3)
[T1, ..., Tn] : list of elements with given types
  - [int, str] accepts [1,”abc”] but not [1,2,3]

---
Types
All variables have types
Types are checked statically when possible
Types play a role during matching:
  - I is int variable, S is str variable, T is term variable
  - match f(13) and f(I?)
  - match f(13) and f(S?)
  - match f(13) and f(T?)
succeeds
fails
succeeds

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
The ToolBus architecture
Coordination
Representation
Computation
ToolBus
Tools
ATerms
common
data exchange
format

---
The ToolBus architecture
Processes inside the ToolBus can communicate with each other
Tools can not communicate with each other
Tools can communicate using a fixed protocol:
ToolBus
ToolBus
ToolBus
Tool
Tool
Tool
eval
value
do
ack-event
event

---
A typical scenario
Configuration knowledge
only in ToolBus script
UI and DB are
completely
decoupled
UI
DB
Database
User-interface

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
ToolBus scripts: processes
The ToolBus: a parallel composition of processes
Private variables per process
P1+ P2 P1. P2 P1|| P2 P1* P2
:=, if then else
All data are terms that can be matched
A limited set of built-in operations on terms
No other support for datatypes

---
ToolBus scripts: processes
Send, receive message (handshaking)
Send/receive notes (broadcasting)
Subscription to notes
Dynamic process creation
Absolute/relative delay, timeout

---
ToolBus scripts: tools
Execute/terminate tools
Connect/disconnect tools
Communication between process and tool is synchronous
Process can send evaluation request to tool (which returns a value later on)
Tool can generate events to be handled by the ToolBus

---
Hello World
The Tscript hello.tb
Define the process HELLO
It only prints a string
process HELLO is printf(“Hello world, my first Tscript!\n”)
toolbus(HELLO)
Define the initial processes
in the application
Start application with: toolbus hello.tb

---
Hello World: string generated by tool
H will represent the tool
process HELLO is
  let H : hello,
        S : str
  in
        execute(hello, H?) .
        snd-eval(H, get-text) .
        rec-value(H, text(S?)) .
        printf(S)
  endlet
tool hello is {command = “hello” }
toolbus(HELLO)
S is a string variable
Execute hello,
H gets a tool id as value
Request a text from hello tool
Receive it,
S gets the value assigned
Definition of hello tool:
may be written in any language

---
Simple clock with user-interface
UI
CLOCK
ToolBus
User can push
a showTime
button
Provides a readTime
function
ui
clock
Tools
Clock
User-interface

---
Simple clock with user-interface
process CLOCK is process-expression-1
tool clock is tool-definition-1
process UI is process-expression-2
tool ui is tool-definition-2
toolbus(CLOCK, UI)

---
Clock
process CLOCK is
    let Tid : clock, T : str
    in
        execute(clock, Tid?).
        (
        rec-msg(showTime) .
        snd-eval(Tid, readTime) .
        rec-value(Tid, time(T?)) .
        snd-msg(showTime, T)
        ) * delta
    endlet
Receive a message from
another process
Get time from clock tool
Reply to the message
( ... ) * delta is an
endless loop
tool clock is { command = “clock” }

---
User-interface
process UI is
   let Tid : ui, T : str
   in
        execute(ui, Tid?) .
        ( rec-event(Tid, button(showTime)) .
        snd-msg(showTime) .
        rec-msg(showTime, T?) .
        snd-do(Tid, displayTime(T)) .
        snd-ack-event(Tid, button(showTime))
        ) * delta
  endlet
Receive event from ui tool
Get the time
Display it in ui tool
Processing of the event
complete: send
acknowledgement
tool ui is { command = “wish-adapter -script ui.tcl” }

---
Tscripts: revisited
Process communication: messages & notes
Composite processes
Expressions & built-in functions
Time primitives
Tools

---
Process communication: messages
Messages used for synchronous, two-party communication between processes
snd-msg and rec-msg synchronize sender/receiver
Communication is possible if the arguments match
There is two-way data transfer between sender and receiver (using result variables)

---
Process communication: notes
Notes used for asynchronous, broadcasting communication between processes
Each process must subscribe to the notes it wants to receive
Each process has a private note queue on which snd-note, rec-note and no-note operate

---
Process communication: notes
subscribe to notes of a given form
  - subscribe(compute(<str>,<int>))
unsubscribe from certain notes
snd-note to all subscribers
  - snd-note(compute(E,V))
rec-note: receive a note of a given form
no-note received of given form

---
Composite process expressions
One of the atomic processes mentioned above
delta (deadlock), tau (silent step)
P1+ P2: choice (non-deterministic)
P1. P2: sequential composition
P1|| P2: parallel composition
P1* P2: repetition

---
Composite process expressions
P(T1, T2, ...): a named process (with optional parameters) will be replaced by its definition
create(P(T1, T2, ...), Pid?): dynamic process creation
V := Expr: evaluate Expr and assign result to V
if Expr then P1 else P2 fi
if Expr then P1 fi = if Expr then P1 else delta fi

---
Expressions
An expression is evaluated in the current environment of the process in which it occurs
Constants evaluate to themselves: a
Variables evaluate to their current values
Lists evaluate to a list of their evaluated elements
Some function symbols have a built-in meaning

---
Built-in functions
Booleans: not, and, or
Integers: add, sub, mul, mod, less, less-equal, greater, greater-equal
Lists: first, next, get, put, join, member, subset, diff, inter, size
Miscellaneous: equal, not-equal, process-id, process-name, current-time, quote

---
Time primitives
A (relative or absolute) delay or time out may be associated with each atomic process
Relative time: delay(Expr) or timeout(Expr)
Absolute time: abs-delay(y, mon, d, h, min, s) or abs-timeout(y, mon, d, h, min, s)
Example:
  - printf(“expired”) delay(10)
  - printf(“Renew account”) abs-timeout(2004,4,1,12,0,0)

---
Process definitions
Process definition: process Pname Formals is P
Formals are optional and contain a list of formal parameter names
  - process MakeWave(N : int) is ...
All variables (including formals) must be declared and have a type
let VarDecls in P endlet introduces variables:
  - let E : str, V : int in ... endlet

---
Tools
Tools have to be executed or connected before they can be used
Requires a tool definition: tool ui is { ... }
Introduces a new type, e.g. ui
Execute a tool: execute(ui, Uid?)
Receive connection request: rec-connect(ui, Uid?)
Tool identification is assigned to Uid (of type uid)

---
Tools
snd-terminate: terminate an executing tool
  - snd-terminate(Tid)
rec-disconnect: receive disconnection request from tool
  - rec-disconnect(Uid)
shutdown: terminate the whole ToolBus
  - shutdown(“Auction ends”)

---
Tools
snd-eval, rec-value: request tool to evaluate a term, and receive the resulting value from tool
  - initiative: ToolBus
snd-do: request tool to perform some action, there is no reply
  - initiative: ToolBus
rec-event, snd-ack-event: receive event from tool, acknowledge it after appropriate processing
  - initiative: tool

---
Tscripts
A Tscripts consists of
  - a list of process and tool definitions
  - a single ToolBus configuration
A ToolBus configuration describes the initial set of active processes in the ToolBus:
  - toolbus(Pname1, ..., Pnamen)
  - Eache Pname is optionally followed by parameters

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples
  - calculator; auction; waves

---
Example: calculator
CALC
BATCH
CLOCK
LOG
UI
ToolBus
clock
ui
log
batch
calc
Tools

---
Example: calculator
CALC: the calculation process
BATCH: reads expressions from file, calculates their value, writes result back to file
UI: the user-interface
LOG maintains a log of all calculations
CLOCK provides current time

---
Process CALC
process CALC is
    let Tid : calc, E : str, V : term
    in
        execute(calc, Tid?).
        (
        rec-msg(compute, E?) .
        snd-eval(Tid, expr(E)) . rec-value(Tid, val(V?)) .
        snd-msg(compute, E, V) . snd-note(compute(E, V))
        )* delta
    endlet
tool calc is { command = “calc”}
Receive compute message
Let calc do the computation
Note for the logger
Reply to compute message

---
Process BATCH
process BATCH is
    let Tid : batch, E : str, V : int
    in
        execute(batch, Tid?).
        (
        snd-eval(Tid, fromFile) . rec-value(Tid, expr(E?)) .
        snd-msg(compute, E) . rec-msg(compute, E, V?) .
        snd-do(Tid, toFile(E, V))
        ) * delta
    endlet
tool batch is {command = “batch”}
Get an expression from batch tool
Evaluate expression
Value back to batch tool

---
User-interface
When the user presses Calc, a dialog window appears to enter an expression
The result is diplayed in a separate window
Pressing showLog display all calculations so far
Pressing showTime displays the current time
Pressing Quit ends the application

---
User-interface: process UI
process UI is
    let Tid : ui
    in
        execute(ui, Tid?) .
        ( CALC-BUTTON(Tid) + LOG-BUTTON(Tid))* delta
        ||
        TIME-BUTTON(Tid) * delta
        ||
        QUIT-BUTTON(Tid)
    endlet
tool ui is { command = wish-adapter -script calc.tcl” }
Calc and Log button are exclusive
Time and Quit button are independent

---
User-interface: CALC-BUTTON
process CALC-BUTTON(Tid : ui) is
    let N : int, E : str, V : term
    in
        rec-event(Tid, N?, button(calc)) .
        snd-eval(Tid, get-expr-dialog) .
        ( rec-value(Tid, cancel)
        + rec-value(Tid, expr(E?)) .
        snd-msg(compute, E) .
        rec-msg(compute, E, V?) .
        snd-do(Tid, display-value(V))
        ) . snd-ack-event(Tid, N)
    endlet
Calc button is pressed
Ask for an expression
Get cancel or an expression
Compute expression
and display its value
Acknowledge the button event

---
User-interface: LOG-BUTTON
process LOG-BUTTON(Tid : ui) is
    let N : int, L : term
    in
        rec-event(Tid, N?, button(showLog)) .
        snd-msg(showLog) .
        rec-msg(showLog, L?) .
        snd-do(Tid, display-log(L)) .
        snd-ack-event(Tid, N)
    endlet

---
User-interface: TIME-BUTTON
process TIME-BUTTON(Tid : ui) is
    let N : int, T : str
    in rec-event(Tid, N?, button(showTime)) .
        snd-msg(showTime) .
        rec-msg(showTime, T?) .
        snd-do(Tid, display-time(T)) .
        snd-ack-event(Tid, N)
    endlet
process QUIT-BUTTON(Tid : ui) is
        rec-event(Tid, button(quit)) .
        shutdown("End of calc demo")

---
Process LOG
process LOG is
    let Tid : log, E : str, V : term, L : term
    in subscribe(compute(<str>, <term>)) .
        execute(log, Tid?).
        ( rec-note(compute(E?, V?)) .
        snd-do(Tid, writeLog(E, V))
        +
        rec-msg(showLog) .
        snd-eval(Tid, readLog) .
        rec-value(Tid, history(L?)) .
        snd-msg(showLog, history(L))
        ) * delta
    endlet
Log all calculations
Show the log of calculations

---
Process LOG1
Alternative definition
of logger: maintain the
log in a list
process LOG1 is
    let TheLog : list, E : str, V : term
    in subscribe(compute(<str>, <term>)) .
        TheLog := [] .
        ( rec-note(compute(E?, V?)) .
        TheLog := join(TheLog, [[E, V]])
        +
        rec-msg(showLog) .
        snd-msg(showLog, TheLog)
        ) * delta
    endlet

---
Process CLOCK
process CLOCK is
    let Tid : clock, T : str
    in
        execute(clock, Tid?).
        ( rec-msg(showTime) .
        snd-eval(Tid, readTime) .
        rec-value(Tid, time(T?)) .
        snd-msg(showTime, T)
        ) * delta
    endlet

---
ToolBus Configuration
toolbus (CALC, BATCH, UI, LOG, CLOCK)
Creates the processes for the calculator application
Start calculator application:
toolbus calc.tb

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples
  - calculator; auction; waves

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples
  - calculator; auction; waves

---
Example: distributed auction
Auction
Master
Bidder
Bidder
Auction
Master
Bidder
Bidder
Classical Auction
Distributed Auction
Bidder
Bidder
Bidder
Bidder
Bidder

---
Example: distributed auction
How are bids synchronized?
How to inform bidders about higher bids?
How to decide when the bidding is over and the item is sold?
Bidders may come and go during the auction

---
Example: distributed auction
Auction
ToolBus
master
Tools
Bidder
bidder
Bidder
bidder
Bidder
bidder
...
...

---
Example: distributed auction
The Auction process
  - executes master tool: user-interface of auction master
  - connection/disconnection of new bidders
  - introduces new items for sale (at the initiative of the auction master)
  - controls the bidding provess via OneSale
A Bidder process is created for each new bidder

---
Process Auction
process Auction is
  let Mid : master, Bid : bidder
  in
      execute(master, Mid?) .
      ( ConnectBidder(Mid, Bid?)
      +
        OneSale(Mid)
      ) *
      rec-event(Mid, quit) .
      shutdown("Auction is closed")
  endlet
Execute the master tool
Repeat:
add new bidder between sales,
or
perform one sale
Until:
auction master quits
Close the auction application
tool master is { command = "wish-adapter -script master.tcl" }

---
Process ConnectBidder
process ConnectBidder(Mid : master, Bid : bidder?) is
  let Pid : int, Name : str
  in
     rec-connect(Bid?) .
     create(Bidder(Bid), Pid?) .
     snd-eval(Bid, get-name) .
     rec-value(Bid, name(Name?)) .
     snd-do(Mid, new-bidder(Bid, Name))
  endlet
Receive a connection request
from a new bidder tool
Create a new Bidder process
Ask bidder for its name
Send name to master tool

---
Process OneSale
process OneSale(Mid : master) is
  let Descr : str, %% Description of current item for sale
      InAmount : int, %% Initial amount for item
      Amount : int, %% Current amount
      HighestBid : int, %% Highest bid so far
      Final : bool, %% Did we already issue a final call for bids?
      Sold : bool, %% Is the item sold?
      Bid : bidder %% New bidder tool connected during sale
  in rec-event(Mid, new-item(Descr?, InAmount?)) .
      HighestBid := InAmount .
      snd-note(new-item(Descr, InAmount)) .
      Final := false . Sold := false .
      ( ...
      ) * if Sold then snd-ack-event(Mid, new-item(Descr, InAmount)) fi
  endlet
Where the action is ...

---
Process OneSale
( if not(Sold) then ... fi
+ if not(or(Final, Sold)) then ... fi
+ if and(Final, not(Sold)) then ... fi
+ ConnectBidder(Mid, Bid?) ...
) * if Sold then ... fi

---
Process OneSale
Receive a bid from a bidder
(
+ if not(or(Final, Sold)) then ... fi
+ if and(Final, not(Sold)) then ... fi
+ ConnectBidder(Mid, Bid?) ...
) * if Sold then ... fi
if not(Sold) then
    rec-msg(bid(Bid?, Amount?)) .
    snd-do(Mid, new-bid(Bid, Amount)) .
    if less-equal(Amount, HighestBid) then
        snd-msg(Bid, rejected)
    else
        HighestBid := Amount .
        snd-msg(Bid, accepted) .
        snd-note(update-bid(Amount)) .
        snd-do(Mid, update-highest-bid(Bid, Amount)) .
        Final := false
    fi
fi
Inform auction master about it
Reject bid if it is too low
Remember as highest bid
Inform bidder: bid is accepted
Inform all bidders
Update auction master

---
Process OneSale
Not yet sold, not asked for final bids ...
( if not(Sold) then ... fi
) * if Sold then ... fi
Wait 10 sec, then ask for final bids
+ if not(or(Final, Sold)) then
      snd-note(any-higher-bid) delay(sec(10)) .
      snd-do(Mid, any-higher-bid(10)) .
       Final := true
  fi
+ if and(Final, not(Sold)) then
      snd-note(sold(HighestBid)) delay(sec(10)) .
      Sold := true
   fi
+ ConnectBidder(Mid, Bid?) .
   snd-msg(Bid, new-item(Descr, HighestBid)) .
   Final := false
Inform auction master
Yes, now we have asked for final bids
Not yet sold, but asked for final bids ...
Wait 10 sec, then inform
all bidders that item is sold
Yes, item is now sold
Bidder is connected during sale
Inform new bidder about progress
Restart, final bids (if any)

---
Process Bidder
process Bidder(Bid : bidder) is
  let Descr : str, Amount : int, Acceptance : term
  in
     subscribe(new-item(<str>, <int>)) . subscribe(update-bid(<int>)) .
     subscribe(sold(<int>)) . subscribe(any-higher-bid) .
     ( ...
     )
     * delta
  endlet

---
Get info about
item for
sale after connection
Process Bidder
Same, but normal case
     ( ( rec-msg(Bid, new-item(Descr?, Amount?))
       + rec-note(new-item(Descr?, Amount?))
       + rec-disconnect(Bid) . delta
       ) .
       snd-do(Bid, new-item(Descr, Amount)) .
       ( rec-event(Bid, bid(Amount?)) .
        snd-msg(bid(Bid, Amount)) . rec-msg(Bid, Acceptance?) .
        snd-do(Bid, accept(Acceptance)) . snd-ack-event(Bid, bid(Amount))
       + rec-note(update-bid(Amount?)) . snd-do(Bid, update-bid(Amount))
       + rec-note(any-higher-bid) . snd-do(Bid, any-higher-bid)
       + rec-disconnect(Bid) . delta
       ) *
       rec-note(sold(Amount?)) . snd-do(Bid, sold(Amount))
     ) *
     delta
Disconnect between sales
Inform bidder tool
bidder comes with new bid
Inform bidder
Disconnect during sale
End of this sale sale

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples
  - calculator; auction; waves

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples
  - calculator; auction; waves

---
One-dimensional wave equation
Simulate a string attached at the two end points:
.
.
.
.
.
.
.
.
.
yi(t)
.
.
1 2 3 4 5 6 ... N-1
i

---
One-dimensional wave equation
Amplitude at point i at t+Dt is given by:
yi(t+t) = F(yi(t),yi(t-t),yi-1(t),yi+1(t))
and
F(z1,z2,z3,z4) = 2z1 ­ z2+ (c t/x)2 (z3­2z1+z4)
x: the (small) interval between sampling points
c: constant representing the propagation velocity of the wave

---
Example: wave equation
ToolBus
master
Tools
MakeWave
Pend
...
Pend
P
P
P
P

---
One-dimensional wave equation
Auxiliary process F computes function F
Process P models a sampling point
Process Pend models the end points
Process MakeWave constructs N connected instances of P and two end points
Tool display visualizes the simulation

---
Process F
Compute F(z1,z2,z3,z4) = 2z1 ­ z2+ (c t/x)2 (z3­2z1+z4)
process F(Z1 : real, Z2 : real, Z3 : real, Z4 : real, Res : real?) is
  let CdTdX2 : real
  in
     CdTdX2 := 0.01 .
     Res := radd(rsub(rmul(2.0, Z1), Z2),
        rmul(CdTdX2,
        radd(rsub(Z3, rmul(2.0, Z1)), Z4)))
  endlet
Arbitrary value for (c t/x)2
 2z1 ­ z2+
(c t/x)2 *
(z3­2z1+z4)

---
Process P
process P(Tid : display, L : int, I : int, R : int, Dstart : real, Estart : real) is
  let AL : real, AR : real, D : real, D1 : real, E : real
  in
     D := Dstart . E := Estart .
     ( ( rec-msg(L, I, AL?)
       || rec-msg(R, I, AR?)
       || snd-msg(I, L, E)
       || snd-msg(I, R, E)
       || snd-do(Tid, update(I, E))
       ) .
       D1 := E .
       F(E, D, AL, AR, E?) .
       D := D1
     ) * delta
  endlet
L: left, I: this point, R: right
D, E: amplitutes of this point
Receive amplitudes of neighbours
Send our amplitude to neighbours
Update our amplitude on display
Compute new versions of D and E

---
Process Pend
Index of this end point
Neighbouring point
process Pend(Tid : display, I : int, NB : int) is
  let W : real
  in
   ( rec-msg(NB, I, W?) || snd-msg(I, NB, 0.0) ||
     snd-do(Tid, update(I, 0.0))
   ) * delta
  endlet
Interact with neighbour
Display (constant) amplitude 0 on display

---
Process MakeWave
process MakeWave(N : int) is
  let Tid : display, Id : int, I : int, L : int, R : int
  in
     execute(display, Tid?) .
     snd-do(Tid, mk-wave(N)) .
     create(Pend(Tid, 0, 1), Id?).
     L := sub(N,1) .
     create(Pend(Tid, N, L), Id?) .
     I := 1 .
     if less(I, N) then
        L := sub(I, 1) . R := add(I, 1) .
        create(P(Tid, L, I, R, 1.0, 1.0), Id?) .
        I := add(I, 1)
     fi *
     shutdown("end") delay(sec(60))
  endlet
Execute display tool
and initialize it
Create the two end points
Create the other points
Shutdown after one minute

---
Tool definition and ToolBus configuration
tool display is { command = "wish-adapter -script ui-wave.tcl"}
toolbus(MakeWave(8))

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples
  - calculator; auction; waves

---
Road map
The problem: component interconnection
History & requirements
Terms, types & matching
The ToolBus architecture
ToolBus scripts (Tscripts)
Larger examples
  - calculator; auction; waves
Concluding remarks

---
Not yet discussed: monitors
A tool can act as a monitor for one or more ToolBus processes
Monitors exist in three categories:
  - Loggers
  - Viewers
  - Controllers
Depending on the category, monitors get all info about steps of the monitored processes they need

---
A Monitor
CALC
BATCH
CLOCK
UI
ToolBus
clock
ui
mon
batch
calc
Tools

---
Loggers
Non-interactive = processes don't wait for logger
Non-intrusive = logger can't change process state
Recording of bahaviour of processes
Examples:
  - System logging
  - Generation of play back scripts for UI testing
  - Performance measurement
  - toolbus -logger calc.tb

---
Viewers
Interactive = processes wait for viewer
Non-intrusive = viewer can't change state
Viewing of processes
Monitored processes wait for a continue message before proceeding
Example:
  - Non-intrusive debugger
  - toolbus -viewer calc.tb

---
Controllers
Interactive & Intrusive control over processes
Controlled processes wait for a continue message (containing new state/process expression)
Examples:
  - Intrusive debugger
  - Advanced control applications that perform arbitrary computations on process expression in tool, but want to reuse other ToolBus tools
Not implemented in current version!